## Slide 1: Computer Networking: A Top Down Approach
Seventh Edition
Chapter 7
Wireless and Mobile Networks
Copyright © 2017, 2013, 2010 Pearson Education, Inc. All Rights Reserved
Notes: If this PowerPoint presentation contains mathematical equations, you may need to check that your computer has the following installed:
1) MathType Plugin
2) Math Player (free versions available)
3) NVDA Reader (free versions available)

## Slide 2: Wireless and Mobile Networks
Background:
# wireless (mobile) phone subscribers now exceeds # wired phone subscribers (5-to-1)!
# wireless Internet-connected devices equals # wireline Internet-connected devices
  laptops, Internet-enabled phones promise anytime untethered Internet access
two important (but different) challenges
  wireless: communication over wireless link
  mobility: handling the mobile user who changes point of attachment to network

## Slide 3: Learning Objectives (1 of 6)
7.1 Introduction
Wireless
7.2 Wireless links, characteristics
  C D M A
7.3 I E E E 802.11 wireless LANs (“Wi-Fi”)
7.4 Cellular Internet Access
  architecture
  standards (e.g., 3G, L T E)
Mobility
7.5 Principles: addressing and routing to mobile users
7.6 Mobile I P
7.7 Handling mobility in cellular networks
7.8 Mobility and higher-layer protocols

## Slide 4: Elements of a Wireless Network (1 of 5)

## Slide 5: Elements of a Wireless Network (2 of 5)

## Slide 6: Elements of a Wireless Network (3 of 5)

## Slide 7: Characteristics of Selected Wireless Links

## Slide 8: Elements of a Wireless Network (4 of 5)

## Slide 9: Elements of a Wireless Network (5 of 5)
ad hoc mode
No base stations
Nodes can only transmit to other nodes within link coverage
Nodes organize themselves into a network: route among themselves

## Slide 10: Wireless Network Taxonomy
Blank | Single hop | Multiple hops
Infrastructure (e.g.,APs) | Host connects to base station (WiFi, WiMAX, cellular) which connects to larger Internet | Host may have to relay through several wireless nodes to connect to larger Internet: mesh net
No infrastructure | No base station, no connection to larger Internet (Bluetooth, ad hoc nets) | No base station, no connection to larger Internet. May have to relay to reach other a given wireless node M A N E T, V A N E T

## Slide 11: Learning Objectives (2 of 6)
7.1 Introduction
Wireless
7.2 Wireless links, characteristics
  C D M A
7.3 I E E E 802.11 wireless LANs (“Wi-Fi”)
7.4 Cellular Internet Access
architecture
  standards (e.g., 3G, L T E)
Mobility
7.5 Principles: addressing and routing to mobile users
7.6 Mobile I P
7.7 Handling mobility in cellular networks
7.8 Mobility and higher-layer protocols

## Slide 12: Wireless Link Characteristics (1 of 2)
Important differences from wired link ….
  Decreased signal strength: radio signal attenuates as it propagates through matter (path loss)
  Interference from other sources: standardized wireless network frequencies (e.g., 2.4 GigaHertz) shared by other devices (e.g., phone); devices (motors) interfere as well
  Multipath propagation: radio signal reflects off objects ground, arriving ad destination at slightly different times
…. make communication across (even a point to point) wireless link much more “difficult”

## Slide 13: Wireless Link Characteristics (2 of 2)
S N R: signal-to-noise ratio
  Larger S N R – easier to extract signal from noise (a “good thing”)
  S N R versus B E R tradeoffs
  given physical layer: increase power -> increase S N R ->decrease B E R
  given S N R: choose physical layer that meets B E R requirement, giving highest thruput
    S N R may change with mobility: dynamically adapt physical layer (modulation technique, rate)

## Slide 14: Wireless Network Characteristics (1 of 2)
Multiple wireless senders and receivers create additional problems (beyond multiple access):

## Slide 15: Wireless Network Characteristics (2 of 2)
Hidden terminal problem
B, A hear each other
B, C hear each other
A, C can not hear each other means A, C unaware of their interference at B
Signal attenuation:
B, A hear each other
B, C hear each other
A, C can not hear each other interfering at B

## Slide 16: Code Division Multiple Access (C D M A)
Unique “code” assigned to each user; i.e., code set partitioning
  all users share same frequency, but each user has own “chipping” sequence (i.e., code) to encode data
  allows multiple users to “coexist” and transmit simultaneously with minimal interference (if codes are “orthogonal”)
Encoded signal = (original data) X (chipping sequence)
Decoding: inner-product of encoded signal and chipping sequence

## Slide 17: C D M A Encode/Decode

## Slide 18: C D M A: Two-Sender Interference

## Slide 19: Learning Objectives (3 of 6)
7.1 Introduction
Wireless
7.2 Wireless links, characteristics
  C D M A
7.3 I E E E 802.11 wireless LANs (“Wi-Fi”)
7.4 Cellular Internet Access
architecture
  standards (e.g., 3G, L T E)
Mobility
7.5 Principles: addressing and routing to mobile users
7.6 Mobile I P
7.7 Handling mobility in cellular networks
7.8 Mobility and higher-layer protocols

## Slide 20: I E E E 802.11 Wireless L A N
802.11b
2.4-5 GigaHertz unlicensed spectrum
up to 11 M b p s
direct sequence spread spectrum (D S S S) in physical layer
  all hosts use same chipping code
802.11a
  5-6 GigaHertz range
  up to 54 M b ps
802.11g
  2.4-5 GigaHertz range
  up to 54 M b p s
802.11n: multiple antennae
  2.4-5 GigaHertz range
  up to 200 M b ps
all use C S M A/C A for multiple access
all have base-station and ad-hoc network versions

## Slide 21: 802.11 LAN Architecture
Wireless host communicates with base station
  base station = access point (A P)
Basic Service Set (B S S) (aka “cell”) in infrastructure mode contains:
  wireless hosts
  access point (A P): base station
  ad hoc mode: hosts only

## Slide 22: 802.11: Channels, Association
802.11b: 2.4GigaHertz-2.485GigaHertz spectrum divided into 11 channels at different frequencies
  A P admin chooses frequency for A P
  Interference possible: channel can be same as that chosen by neighboring A P!
Host: must associate with an A P
  scans channels, listening for beacon frames containing A P’s name (S S I D) and M A C address
  selects A P to associate with
  may perform authentication [Chapter 8]
  will typically run D H C P to get I P address in A P’s subnet

## Slide 23: 802.11: Passive/Active Scanning (1 of 2)

## Slide 24: 802.11: Passive/Active Scanning (2 of 2)
Passive scanning:
(1) beacon frames sent from A Ps
(2) association Request frame sent: H1 to selected A P
(3) association Response frame sent from selected A P to H1
Active scanning:
(1) Probe Request frame broadcast from H1
(2) Probe Response frames sent from A Ps
(3) Association Request frame sent: H1 to selected A P
(4) Association Response frame sent from selected A P to H1

## Slide 25: I E E E 802.11: Multiple Access
avoid collisions:
nodes transmitting at same time
802.11: C S M A - sense before transmitting
  Don’t collide with ongoing transmission by other node
802.11: no collision detection!
  Difficult to receive (sense collisions) when transmitting due to weak received signals (fading)
  Can’t sense all collisions in any case: hidden terminal, fading
  Goal: avoid collisions: C S M A/C(ollision)A(voidance)

## Slide 26: I E E E 802.11 M A C Protocol: C S M A /C A
802.11 sender
If sense channel idle for D I F S then transmit entire frame (no C D)
If sense channel busy then start random backoff time timer counts down while channel idle transmit when timer expires if no A C K, increase random backoff interval, repeat 2
802.11 receiver
  If frame received OK return A C K after S I F S (A C K needed due to hidden terminal problem)

## Slide 27: Avoiding collisions
Idea: Allow sender to “reserve” channel rather than random access of data frames: avoid collisions of long data frames
Sender first transmits small request-to-send (R T S) packets to B S using C S M A
  R T Ss may still collide with each other (but they’re short)
B S broadcasts clear-to-send C T S in response to R T S
C T S heard by all nodes
  sender transmits data frame
  other stations defer transmissions
Avoid data frame collisions completely using small reservation packets!

## Slide 28: Collision Avoidance: R T S-C T S exchange

## Slide 29: 802.11 Frame: Addressing (1 of 2)

## Slide 30: 802.11 Frame: Addressing (2 of 2)

## Slide 31: 802.11 Frame: More

## Slide 32: 802.11: Mobility within Same Subnet
H1 remains in same I P subnet: I P address can remain same
Switch: which A P is associated with H1?
  Self-learning (Ch. 5): switch will see frame from H1 and “remember” which switch port can be used to reach H1

## Slide 33: 802.11: Advanced Capabilities (1 of 2)
Rate adaptation
Base station, mobile dynamically change transmission rate (physical layer modulation technique) as mobile moves, S N R varies
S N R decreases, B E R increase as node moves away from base station
When B E R becomes too high, switch to lower transmission rate but with lower B E R

## Slide 34: 802.11: Advanced Capabilities (2 of 2)
Power management
node-to-A P: “I am going to sleep until next beacon frame”
  A P knows not to transmit frames to this node
  node wakes up before next beacon frame
Beacon frame: contains list of mobiles with A P-to-mobile frames waiting to be sent
  Node will stay awake if A P-to-mobile frames to be sent; otherwise sleep again until next beacon frame

## Slide 35: 802.15: Personal Area Network
Less than 10 meter diameter
Replacement for cables (mouse, keyboard, headphones)
ad hoc: no infrastructure
Master/Slaves:
  Slaves request permission to send (to master)
  Master grants requests
802.15: Evolved from Bluetooth specification
  2.4-2.5 GigaHertz radio band
  up to 721 k b p s

## Slide 36: Learning Objectives (4 of 6)
7.1 Introduction
Wireless
7.2 Wireless links, characteristics
  C D M A
7.3 I E E E 802.11 wireless LANs (“Wi-Fi”)
7.4 Cellular Internet Access
architecture
  standards (e.g., 3G, L T E)
Mobility
7.5 Principles: addressing and routing to mobile users
7.6 Mobile I P
7.7 Handling mobility in cellular networks
7.8 Mobility and higher-layer protocols

## Slide 37: Components of Cellular Network Architecture (1 of 2)

## Slide 38: Cellular Networks: The First Hop
Two techniques for sharing mobile-to-B S radio spectrum
Combined F D M A/T D M A: divide spectrum in frequency channels, divide each channel into time slots
C D M A: code division multiple access

## Slide 39: 2G (voice) Network Architecture

## Slide 40: 3G (voice+data) Network Architecture (1 of 2)
Key insight: new cellular data network operates in parallel (except at edge) with existing cellular voice network
voice network unchanged in core
data network operates in parallel

## Slide 41: 3G (voice+data) Network Architecture (2 of 2)

## Slide 42: 3G versus 4G L T E Network Architecture

## Slide 43: 4G: Differences from 3G
all I P core: I P packets tunneled (through core I P network) from base station to gateway
no separation between voice and data – all traffic carried over I P core to gateway

## Slide 44: Functional Split of Major L T E Components

## Slide 45: Radio+Tunneling: U E – eNodeB – P G W

## Slide 46: Quality of Service in L T E
Q o S from eNodeB to S G W: min and max guaranteed bit rate
Q o S in radio access network: one of 12 Q C I values
Q C I | Resource type | Priority | Packet delay Budget (ms) | Packet error loss rate | Example services
1 | G B R | 2 | 100 | 10 to the negative second power | Conversational voice
2 | G B R | 4 | 150 | 10 to the negative third power | Conversational video (live streaming)
3 | G B R | 5 | 300 | 10 to the negative six power | Non-conversational video (buffer streaming)
4 | G B R | 3 | 50 | 10 to the negative third power | Real-time gaming
5 | Non-G B R | 1 | 100 | 10 to the negative six power | I M S signaling
6 | Non-G B R | 7 | 100 |  | Voice ,video (live streaming),interactive gaming
7 | Non-G B R | 6 | 300 | 10 to the negative six power | Video (buffer streaming)
8 | Non-G B R | 8 | 300 | 10 to the negative six power | TCP-based (for example,WWW,e-mail),chat,FTP,p2p file sharing,Progressive video and others
9 | Non-G B R | 9 | 300 | 10 to the negative six power | 

## Slide 47: Learning Objectives (5 of 6)
7.1 Introduction
Wireless
7.2 Wireless links, characteristics
  C D M A
7.3 I E E E 802.11 wireless LANs (“Wi-Fi”)
7.4 Cellular Internet Access
architecture
  standards (e.g., 3G, L T E)
Mobility
7.5 Principles: addressing and routing to mobile users
7.6 Mobile I P
7.7 Handling mobility in cellular networks
7.8 Mobility and higher-layer protocols

## Slide 48: What is Mobility?
spectrum of mobility, from the network perspective:

## Slide 49: Mobility: Vocabulary

## Slide 50: Mobility: More Vocabulary

## Slide 51: How Do You Contact a Mobile Friend
Consider friend frequently changing addresses, how do you find her?
Search all phone books?
Call her parents?
Expect her to let you know where he/she is?
Facebook!

## Slide 52: Mobility: Approaches (1 of 2)
let routing handle it: routers advertise permanent address of mobile-nodes-in-residence via usual routing table exchange.
  routing tables indicate where each mobile located
  no changes to end-systems
let end-systems handle it:
  Indirect routing: communication from correspondent to mobile goes through home agent, then forwarded to remote
  Direct routing: correspondent gets foreign address of mobile, sends directly to mobile

## Slide 53: Mobility: Approaches (2 of 2)
let end-systems handle it:
  Indirect routing: communication from correspondent to mobile goes through home agent, then forwarded to remote
  Direct routing: correspondent gets foreign address of mobile, sends directly to mobile

## Slide 54: Mobility: Registration
End result:
Foreign agent knows about mobile
Home agent knows location of mobile

## Slide 55: Mobility via Indirect Routing

## Slide 56: Indirect Routing: Comments
Mobile uses two addresses:
  Permanent address: used by correspondent (hence mobile location is transparent to correspondent)
  Care-of-address: used by home agent to forward datagrams to mobile
Foreign agent functions may be done by mobile itself
Triangle routing: correspondent-home-network-mobile
  inefficient when correspondent, mobile are in same network

## Slide 57: Indirect Routing: Moving Between Networks
Suppose mobile user moves to another network
  registers with new foreign agent
  new foreign agent registers with home agent
  home agent update care-of-address for mobile
  packets continue to be forwarded to mobile (but with new care-of-address)
Mobility, changing foreign networks transparent: on going connections can be maintained!

## Slide 58: Mobility via Direct Routing

## Slide 59: Mobility via Direct Routing: Comments
overcome triangle routing problem
non-transparent to correspondent: correspondent must get care-of-address from home agent
  what if mobile changes visited network?

## Slide 60: Accommodating Mobility with Direct Routing
Anchor foreign agent: F A in first visited network
Data always routed first to anchor F A
When mobile moves: new F A arranges to have data forwarded from old F A (chaining)

## Slide 61: Learning Objectives (6 of 6)
7.1 Introduction
Wireless
7.2 Wireless links, characteristics
  C D M A
7.3 I E E E 802.11 wireless LANs (“Wi-Fi”)
7.4 Cellular Internet Access
architecture
  standards (e.g., 3G, L T E)
Mobility
7.5 Principles: addressing and routing to mobile users
7.6 Mobile I P
7.7 Handling mobility in cellular networks
7.8 Mobility and higher-layer protocols

## Slide 62: Mobile I P
R F C 3344
Has many features we’ve seen:
  home agents, foreign agents, foreign-agent registration, care-of-addresses, encapsulation (packet-within-a-packet)
Three components to standard:
  indirect routing of datagrams
  agent discovery
  registration with home agent

## Slide 63: Mobile I P: Indirect routing

## Slide 64: Mobile I P: Agent discovery
Agent Advertisement: Foreign/Home agents advertise service by broadcasting I C M P messages (typefield = 9)

## Slide 65: Mobile I P: Registration Example

## Slide 66: Components of Cellular Network Architecture (2 of 2)

## Slide 67: Handling Mobility in Cellular networks
Home Network: network of cellular provider you subscribe to (e.g., Sprint P C S, Verizon)
  Home location register (H L R): database in home network containing permanent cell phone #, profile information (services, preferences, billing), information about current location (could be in another network)
Visited Network: network in which mobile currently resides
  Visitor location register (V L R): database with entry for each user currently in network
  could be home network

## Slide 68: G S M: Indirect Routing to Mobile

## Slide 69: G S M: Handoff with Common M S C (1 of 2)
Handoff goal: route call via new base station (without interruption)
Reasons for handoff:
  stronger signal to/from new B S S (continuing connectivity, less battery drain)
  load balance: free up channel in current B S S
  G S M doesn’t mandate why to perform handoff (policy), only how (mechanism)
Handoff initiated by old B S S

## Slide 70: G S M: Handoff with Common M S C (2 of 2)
Old B S S informs M S C of impending handoff, provides list of
new B S Ss
MSC sets up path (allocates resources) to new B S S
New B S S allocates radio channel for use by mobile
New B S S signals M S C, old B S S: ready
Old B S S tells mobile: perform handoff to new B S S
Mobile, new B S S signal to activate new channel
Mobile signals via new B S S to M S C : handoff complete.
M S C reroutes call resources released

## Slide 71: G S M: Handoff Between M S Cs (1 of 2)
Anchor M S.C: first M S.C visited during call
  call remains routed through anchor M S.C
new M S.Cs add on to end of M S.C chain as mobile moves to new M S.C
optional path minimization step to shorten multi-M S.C chain

## Slide 72: G S M: Handoff Between M S Cs (2 of 2)
Anchor M S.C: first M S.C visited during call
  call remains routed through anchor M S.C
new M S.Cs add on to end of M S.C chain as mobile moves to new M S.C
optional path minimization step to shorten multi-M S.C chain

## Slide 73: Handling Mobility in L T E
Paging: idle U E may move from cell to cell: network does not know where the idle U E is resident
  paging message from M M E broadcast by all eNodeB to locate U E
Handoff: similar to 3G:
  preparation phase
  execution phase
  completion phase

## Slide 74: Mobility: Cellular Versus Mobile I P
Cellular element | Comment on cellular element | Mobile IP element
Home system | Network to which mobile user’s permanent phone number belongs | Home network
Gateway Mobile Switching Center, or “home M S C”. Home Location Register (H L R) | Home M S C: point of contact to obtain routable address of mobile user. H L R: database in home system containing permanent phone number, profile information, current location of mobile user, subscription information | Home agent
Visited System | Network other than home system where mobile user is currently residing | Visited network
Visited Mobile services Switching Center. Visitor Location Record (V L R) | Visited M S C: responsible for setting up calls to/from mobile nodes in cells associated with M S C. V L R: temporary database entry in visited system, containing subscription information for each visiting mobile user | Foreign agent
Mobile Station Roaming Number (M S R N), or “roaming number” | Routable address for telephone call segment between home M S C and visited M S C, visible to neither the mobile nor the correspondent. | Care-of-address

## Slide 75: Wireless, Mobility: Impact on Higher Layer Protocols
Logically, impact should be minimal …
  best effort service model remains unchanged
  T C P and U D P can (and do) run over wireless, mobile
… but performance-wise:
  packet loss/delay due to bit-errors (discarded packets, delays for link-layer retransmissions), and handoff
  T C P interprets loss as congestion, will decrease congestion window un-necessarily
  delay impairments for real-time traffic
  limited bandwidth of wireless links

## Slide 76: Chapter summary (1 of 2)
Wireless
wireless links:
  capacity, distance
  channel impairments
  C D M A
I E E E 802.11 (“Wi-Fi”)
  C S M A/C A reflects wireless channel characteristics
cellular access
  architecture
  standards (e.g., 3G, 4G L T E)

## Slide 77: Chapter summary (2 of 2)
Mobility
principles: addressing, routing to mobile users
  home, visited networks
  direct, indirect routing
  care-of-addresses
case studies
  mobile I P
  mobility in G S M, L T E
impact on higher-layer protocols

## Slide 78: Copyright