## Slide 1: Computer Networking: A Top Down Approach
Seventh Edition
Chapter 6
The Link Layer and LANs
Copyright © 2017, 2013, 2010 Pearson Education, Inc. All Rights Reserved
Slides in this presentation contain hyperlinks. JAWS users should be able to get a list of links by using INSERT+F7
Notes: If this PowerPoint presentation contains mathematical equations, you may need to check that your computer has the following installed:
1) MathType Plugin
2) Math Player (free versions available)
3) NVDA Reader (free versions available)

## Slide 2: Link Layer and LANs
our goals:
understand principles behind link layer services:
  error detection, correction
  sharing a broadcast channel: multiple access
  link layer addressing
  local area networks: Ethernet, V LANs
instantiation, implementation of various link layer technologies

## Slide 3: Learning Objectives (1 of 9)
6.1 introduction, services
6.2 error detection, correction
6.3 multiple access protocols
6.4 LANs
  addressing, A R P
  Ethernet
  switches
  V LANS
6.5 link virtualization: M P L S
6.6 data center networking
6.7 a day in the life of a web request

## Slide 4: Link Layer: Introduction
terminology:
hosts and routers: nodes
communication channels that connect adjacent nodes along communication path: links
  wired links
  wireless links
  LANs
layer-2 packet: frame, encapsulates datagram
data-link layer has responsibility of transferring datagram from one node to physically adjacent node over a link

## Slide 5: Link Layer: Context
datagram transferred by different link protocols over different links:
  e.g., Ethernet on first link, frame relay on intermediate links, 802.11 on last link
each link protocol provides different services
  e.g., may or may not provide r d t over link
  transportation analogy:
trip from Princeton to Lausanne
  limo: Princeton to J F K
  plane: J F K to Geneva
  train: Geneva to Lausanne
tourist = datagram
transport segment = communication link
transportation mode = link layer protocol
travel agent = routing algorithm

## Slide 6: Link Layer Services (1 of 2)
framing, link access:
  encapsulate datagram into frame, adding header, trailer
  channel access if shared medium
  “MAC” addresses used in frame headers to identify source, destination
    different from I P address!
reliable delivery between adjacent nodes
  we learned how to do this already (chapter 3)!
  seldom used on low bit-error link (fiber, some twisted pair)
  wireless links: high error rates
    Q: why both link-level and end-end reliability?

## Slide 7: Link Layer Services (2 of 2)
flow control:
  pacing between adjacent sending and receiving nodes
error detection:
  errors caused by signal attenuation, noise.
  receiver detects presence of errors:
    signals sender for retransmission or drops frame
error correction:
  receiver identifies and corrects bit error(s) without resorting to retransmission
half-duplex and full-duplex
  with half duplex, nodes at both ends of link can transmit, but not at same time

## Slide 8: Where is the Link Layer Implemented?
in each and every host
link layer implemented in “adaptor” (aka network interface card N I C) or on a chip
  Ethernet card, 802.11 card; Ethernet chipset
  implements link, physical layer
attaches into host’s system buses
combination of hardware, software, firmware

## Slide 9: Adaptors Communicating
sending side:
  encapsulates datagram in frame
  adds error checking bits, rdt, flow control, etc.
receiving side
  looks for errors, rdt, flow control, etc.
  extracts datagram, passes to upper layer at receiving side

## Slide 10: Learning Objectives (2 of 9)
6.1 introduction, services
6.2 error detection, correction
6.3 multiple access protocols
6.4 LANs
  addressing, A R P
  Ethernet
  switches
  V LANS
6.5 link virtualization: M P L S
6.6 data center networking
6.7 a day in the life of a web request

## Slide 11: Error Detection
E D C = Error Detection and Correction bits (redundancy)
D = Data protected by error checking, may include header fields
Error detection not 100% reliable!
  protocol may miss some errors, but rarely
  larger E D C field yields better detection and correction

## Slide 12: Parity Checking
single bit parity:
detect single bit errors
two-dimensional bit parity:
detect and correct single bit errors
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 13: Internet Checksum (Review)
goal: detect “errors” (e.g., flipped bits) in transmitted packet (note: used at transport layer only)
sender:
treat segment contents as sequence of 16-bit integers
checksum: addition (1’s complement sum) of segment contents
sender puts checksum value into U D P checksum field
receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected. But maybe errors nonetheless?

## Slide 14: Cyclic Redundancy Check
more powerful error-detection coding
view data bits, D, as a binary number
choose r+1 bit pattern (generator), G
goal: choose r C R C bits, R, such that
  <D,R> exactly divisible by G (modulo 2)
  receiver knows G, divides <D,R> by G. If non-zero remainder: error detected!
  can detect all burst errors less than r+1 bits
widely used in practice (Ethernet, 802.11 WiFi, A T M)

## Slide 15: C R C Example
want:
equivalently:
equivalently:
if we divide
by G, want remainder R to satisfy:
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 16: Learning Objectives (3 of 9)
6.1 introduction, services
6.2 error detection, correction
6.3 multiple access protocols
6.4 LANs
  addressing, A R P
  Ethernet
  switches
  V LANS
6.5 link virtualization: M P L S
6.6 data center networking
6.7 a day in the life of a web request

## Slide 17: Multiple Access Links, Protocols
two types of “links”:
point-to-point
  P P P for dial-up access
  point-to-point link between Ethernet switch, host
broadcast (shared wire or medium)
  old-fashioned Ethernet
  upstream H F C
  802.11 wireless LAN

## Slide 18: Multiple Access Protocols
single shared broadcast channel
two or more simultaneous transmissions by nodes: interference
  collision if node receives two or more signals at the same time
multiple access protocol
distributed algorithm that determines how nodes share channel, i.e., determine when node can transmit
communication about channel sharing must use channel itself!
  no out-of-band channel for coordination

## Slide 19: An Ideal Multiple Access Protocol
given: broadcast channel of rate R bps
desiderata:
  when one node wants to transmit, it can send at rate R.
  when M nodes want to transmit, each can send at average rate R/M
  fully decentralized:
    no special node to coordinate transmissions
    no synchronization of clocks, slots
simple

## Slide 20: M A C Protocols: Taxonomy
three broad classes:
channel partitioning
  divide channel into smaller “pieces” (time slots, frequency, code)
  allocate piece to node for exclusive use
random access
  channel not divided, allow collisions
  “recover” from collisions
“taking turns”
  nodes take turns, but nodes with more to send can take longer turns

## Slide 21: Channel Partitioning MAC Protocols: T D M A
T D M A: time division multiple access
access to channel in “rounds”
each station gets fixed length slot (length = packet transmission time) in each round
unused slots go idle
example: 6-station LAN, 1,3,4 have packets to send, slots 2,5,6 idle

## Slide 22: Channel Partitioning MAC Protocols: F D M A
F D M A: frequency division multiple access
channel spectrum divided into frequency bands
each station assigned fixed frequency band
unused transmission time in frequency bands go idle
example: 6-station LAN, 1,3,4 have packet to send, frequency bands 2,5,6 idle

## Slide 23: Random Access Protocols
when node has packet to send
  transmit at full channel data rate R.
  no a priori coordination among nodes
two or more transmitting nodes → “collision”,
random access MAC protocol specifies:
  how to detect collisions
  how to recover from collisions (e.g., via delayed retransmissions)
examples of random access MAC protocols:
  slotted A L O H A
  A L O H A
  C S M A, C S M A/C D, C S M A/C A

## Slide 24: Slotted A L O H A (1 of 2)
assumptions:
all frames same size
time divided into equal size slots (time to transmit 1 frame)
nodes start to transmit only slot beginning
nodes are synchronized
if 2 or more nodes transmit in slot, all nodes detect collision
operation:
when node obtains fresh frame, transmits in next slot
  if no collision: node can send new frame in next slot
  if collision: node retransmits frame in each subsequent slot with prob. p until success

## Slide 25: Slotted A L O H A (2 of 2)
Pros:
single active node can continuously transmit at full rate of channel
highly decentralized: only slots in nodes need to be in sync
simple
Cons:
collisions, wasting slots
idle slots
nodes may be able to detect collision in less than time to transmit packet
clock synchronization

## Slide 26: Slotted A L O H A: Efficiency (1 of 2)
efficiency: long-run fraction of successful slots (many nodes, all with many frames to send)
suppose: N nodes with many frames to send, each transmits in slot with probability p
prob that given node has success in a slot
prob that any node has a success

## Slide 27: Slotted A L O H A: Efficiency (2 of 2)
max efficiency: find
that maximizes
for many nodes, take limit of
as N goes to infinity, gives:
at best: channel used for useful transmissions 37% of time!

## Slide 28: Pure (Unslotted) A L O H A
unslotted Aloha: simpler, no synchronization
when frame first arrives
  transmit immediately
collision probability increases:
  frame sent at t0 collides with other frames sent in [t0-1,t0+1]

## Slide 29: Pure A L O H A Efficiency
P(success by given node) = P(node transmits)
P(no other node transmits in [t0-1,t0]
P(no other node transmits in [t0-1,t0]
… choosing optimum p and then letting
even worse than slotted Aloha!

## Slide 30: C S M A (Carrier Sense Multiple Access)
C S M A: listen before transmit:
if channel sensed idle: transmit entire frame
if channel sensed busy, defer transmission
human analogy: don’t interrupt others!

## Slide 31: C S M A Collisions
collisions can still occur: propagation delay means two nodes may not hear each other’s transmission
collision: entire packet transmission time wasted
  distance & propagation delay play role in in determining collision probability

## Slide 32: C S M A/C D (Collision Detection) (1 of 2)
C S M A/C D: carrier sensing, deferral as in C S M A
  collisions detected within short time
  colliding transmissions aborted, reducing channel wastage
collision detection:
  easy in wired LANs: measure signal strengths, compare transmitted, received signals
  difficult in wireless LANs: received signal strength overwhelmed by local transmission strength
human analogy: the polite conversationalist

## Slide 33: C S M A/C D (Collision Detection) (2 of 2)

## Slide 34: Ethernet C S M A/C D Algorithm
N I C receives datagram from network layer, creates frame
If N I C senses channel idle, starts frame transmission. If N I C senses channel busy, waits until channel idle, then transmits.
If N I C transmits entire frame without detecting another transmission, N I C is done with frame !
If N I C detects another transmission while transmitting, aborts and sends jam signal
After aborting, N I C enters binary (exponential) backoff:
after mth collision, N I C chooses K at random from
  N I C waits K·512 bit times, returns to Step 2
  longer backoff interval with more collisions

## Slide 35: C S M A/C D Efficiency
Tprop = max prop delay between 2 nodes in LAN
ttrans = time to transmit max-size frame
efficiency goes to 1
  as tprop goes to 0
  as ttrans goes to infinity
better performance than A L O H A: and simple, cheap, decentralized!

## Slide 36: “Taking Turns” MAC Protocols (1 of 3)
channel partitioning MAC protocols:
  share channel efficiently and fairly at high load
  inefficient at low load: delay in channel access, 1/N bandwidth allocated even if only 1 active node!
random access MAC protocols
  efficient at low load: single node can fully utilize channel
  high load: collision overhead
“taking turns” protocols
  look for best of both worlds!

## Slide 37: “Taking Turns” MAC Protocols (2 of 3)
polling:
master node “invites” slave nodes to transmit in turn
typically used with “dumb” slave devices
concerns:
  polling overhead
  latency
  single point of failure (master)np

## Slide 38: “Taking Turns” MAC Protocols (3 of 3)
token passing:
control token passed from one node to next sequentially.
token message
concerns:
  token overhead
  latency
  single point of failure (token)

## Slide 39: Cable Access Network (1 of 2)
multiple 40 M b p s downstream (broadcast) channels
  single C M T S transmits into channels
multiple 30 M b p s upstream channels
  multiple access: all users contend for certain upstream channel time slots (others assigned)

## Slide 40: Cable Access Network (2 of 2)
D O C S I S: data over cable service interface spec
F D M over upstream, downstream frequency channels
T D M upstream: some slots assigned, some have contention
  downstream M A P frame: assigns upstream slots
  request for upstream slots (and data) transmitted random access (binary backoff) in selected slots

## Slide 41: Summary of MAC Protocols
channel partitioning, by time, frequency or code
  Time Division, Frequency Division
random access (dynamic),
  A L O H A, S-A L O H A, C S M A, C S M A/C D
  carrier sensing: easy in some technologies (wire), hard in others (wireless)
  C S M A / C D used in Ethernet
  C S M A / C A used in 802.11
taking turns
  polling from central site, token passing
  Bluetooth, F D D I, token ring

## Slide 42: Learning Objectives (4 of 9)
6.1 introduction, services
6.2 error detection, correction
6.3 multiple access protocols
6.4 LANs
  addressing, A R P
  Ethernet
  switches
  V LANS
6.5 link virtualization: M P L S
6.6 data center networking
6.7 a day in the life of a web request

## Slide 43: MAC Addresses and A R P
32-bit I P address:
  network-layer address for interface
  used for layer 3 (network layer) forwarding
MAC (or LAN or physical or Ethernet) address:
  function: used ‘locally” to get frame from one interface to another physically-connected interface (same network, in I P-addressing sense)
  48 bit MAC address (for most LANs) burned in N I C R O M, also sometimes software settable
  e.g.: 1 A-2 F-B B-76-09-A D

## Slide 44: LAN Addresses and A R P
each adapter on LAN has unique LAN address

## Slide 45: LAN Addresses
MAC address allocation administered by I E E E
manufacturer buys portion of MAC address space (to assure uniqueness)
analogy:
  MAC address: like Social Security Number
  I P address: like postal address
MAC flat address → portability
  can move LAN card from one LAN to another
I P hierarchical address not portable
  address depends on I P subnet to which node is attached

## Slide 46: A R P: Address Resolution Protocol
Question: how to determine interface’s M A C address, knowing its IP address?
A R P table: each I P node (host, router) on LAN has table
  I P/MAC address mappings for some LAN nodes:
  < I P address; MAC address; T T L>
  T T L (Time To Live): time after which address mapping will be forgotten (typically 20 min)

## Slide 47: A R P Protocol: Same LAN (1 of 2)
A wants to send datagram to B
  B’s MAC address not in A’s A R P table.
A broadcasts A R P query packet, containing B’s I P address
  destination M A C address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive A R P query
B receives A R P packet, replies to A with its (B’s) M A C address
  frame sent to A’s MAC address (unicast)

## Slide 48: A R P Protocol: Same LAN (2 of 2)
A caches (saves) I P-to-MAC address pair in its A R P table until information becomes old (times out)
  soft state: information that times out (goes away) unless refreshed
A R P is “plug-and-play”:
  nodes create their A R P tables without intervention from net administrator

## Slide 49: Addressing: Routing to Another LAN (1 of 5)
walkthrough: send datagram from A to B via R
  focus on addressing – at I P (datagram) and MAC layer (frame)
  assume A knows B’s I P address
  assume A knows I P address of first hop router, R (how?)
  assume A knows R’s MAC address (how?)

## Slide 50: Addressing: Routing to Another LAN (2 of 5)
A creates I P datagram with I P source A, destination B
A creates link-layer frame with R’s MAC address as destination address, frame contains A-to-B I P datagram

## Slide 51: Addressing: Routing to Another LAN (3 of 5)
frame sent from A to R
frame received at R, datagram removed, passed up to I P

## Slide 52: Addressing: Routing to Another LAN (4 of 5)
R forwards datagram with I P source A, destination B
R creates link-layer frame with B‘s MAC address as destination address, frame contains A-to-B I P datagram

## Slide 53: Addressing: Routing to Another LAN (5 of 5)
R forwards datagram with I P source A, destination B
R creates link-layer frame with B's MAC address as dest, frame contains A-to-B I P datagram
Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 54: Learning Objectives (5 of 9)
6.1 introduction, services
6.2 error detection, correction
6.3 multiple access protocols
6.4 LANs
  addressing, A R P
  Ethernet
  switches
  V LANS
6.5 link virtualization: M P L S
6.6 data center networking
6.7 a day in the life of a web request

## Slide 55: Ethernet
“dominant” wired LAN technology:
single chip, multiple speeds (e.g., Broadcom B C M 5761)
first widely used LAN technology
simpler, cheap
kept up with speed race: 10 M b p s – 10 G b p s
Metcalfe’s Ethernet sketch

## Slide 56: Ethernet: Physical Topology
bus: popular through mid 90s
  all nodes in same collision domain (can collide with each other)
star: prevails today
  active switch in center
  each “spoke” runs a (separate) Ethernet protocol (nodes do not collide with each other)
bus: coaxial cable
star

## Slide 57: Ethernet Frame Structure (1 of 2)
sending adapter encapsulates I P datagram (or other network layer protocol packet) in Ethernet frame
preamble:
7 bytes with pattern 10101010 followed by one byte with pattern 10101011
used to synchronize receiver, sender clock rates

## Slide 58: Ethernet Frame Structure (2 of 2)
addresses: 6 byte source, destination MAC addresses
  if adapter receives frame with matching destination address, or with broadcast address (e.g. A R P packet), it passes data in frame to network layer protocol
  otherwise, adapter discards frame
type: indicates higher layer protocol (mostly I P but others possible, e.g., Novell I P X, AppleTalk)
C R C: cyclic redundancy check at receiver
  error detected: frame is dropped

## Slide 59: Ethernet: Unreliable, Connectionless
connectionless: no handshaking between sending and receiving N I C s
unreliable: receiving N I C doesn't send acks or nacks to sending N I C
  data in dropped frames recovered only if initial sender uses higher layer rdt (e.g., T C P), otherwise dropped data lost
Ethernet’s MAC protocol: unslotted C S M A/C D with binary backoff

## Slide 60: 802.3 Ethernet Standards: Link & Physical Layers
many different Ethernet standards
  common MAC protocol and frame format
  different speeds: 2 M b p s, 10 M b p s, 100 M b p s, 1G b p s, 10 G b3p s, 40 G b p s
  different physical layer media: fiber, cable

## Slide 61: Learning Objectives (6 of 9)
6.1 introduction, services
6.2 error detection, correction
6.3 multiple access protocols
6.4 LANs
  addressing, A R P
  Ethernet
  switches
  V LANS
6.5 link virtualization: M P L S
6.6 data center networking
6.7 a day in the life of a web request

## Slide 62: Ethernet Switch
link-layer device: takes an active role
  store, forward Ethernet frames
  examine incoming frame’s M A C address, selectively forward frame to one-or-more outgoing links when frame is to be forwarded on segment, uses C S M A/ C D to access segment
transparent
  hosts are unaware of presence of switches
plug-and-play, self-learning
  switches do not need to be configured

## Slide 63: Switch: Multiple Simultaneous Transmissions
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link, but no collisions; full duplex
  each link is its own collision domain
switching: A-to-A’ and B-to-B’ can transmit simultaneously, without collisions

## Slide 64: Switch Forwarding Table
Q: how does switch know A’ reachable via interface 4, B’ reachable via interface 5?
A: each switch has a switch table, each entry:
  (M A C address of host, interface to reach host, time stamp)
  looks like a routing table!
Q: how are entries created, maintained in switch table?
  something like a routing protocol?

## Slide 65: Switch: Self-Learning
switch learns which hosts can be reached through which interfaces
  when frame received, switch “learns” location of sender: incoming LAN segment
  records sender/location pair in switch table
Switch table (initially empty)
MAC addr | interface | T T L
A | 1 | 60

## Slide 66: Switch: Frame Filtering/Forwarding
when frame received at switch:
record incoming link, MAC address of sending host
index switch table using MAC destination address
if entry found for destination
then {
  if destination on segment from which frame arrived then drop frame
  else forward frame on interface indicated by entry
  }
  else flood /* forward on all interfaces except arriving interface */

## Slide 67: Self-Learning, Forwarding: Example
frame destination, A’, location unknown:flood
destination A location known:selectively send on just one link
MAC addr | interface | TTL
A A’ | 1 4 | 60 60
switch table (initially empty)

## Slide 68: Interconnecting Switches
self-learning switches can be connected together:
Q: sending from A to G - how does S1 know to forward frame destined to G via S4 and S3?
A: self learning! (works exactly the same as in single-switch case!)

## Slide 69: Self-Learning Multi-Switch Example
Suppose C sends frame to I, I responds to C
Q: show switch tables and packet forwarding in S1, S2, S3, S4

## Slide 70: Institutional Network

## Slide 71: Switches vs. Routers
both are store-and-forward:
routers: network-layer devices (examine network-layer headers)
switches: link-layer devices (examine link-layer headers)
both have forwarding tables:
routers: compute tables using routing algorithms, I P addresses
switches: learn forwarding table using flooding, learning, MAC addresses

## Slide 72: V LANs: Motivation
consider:
C S user moves office to E E, but wants connect to C S switch?
single broadcast domain:
  all layer-2 broadcast traffic (A R P, D H C P, unknown location of destination MAC address) must cross entire LAN
  security/privacy, efficiency issues

## Slide 73: V LANs
Virtual Local Area Network
switch(e s) supporting V LAN capabilities can be configured to define multiple virtual LANS over single physical LAN infrastructure.
port-based V LAN: switch ports grouped (by switch management software) so that single physical switch ……
… operates as multiple virtual switches

## Slide 74: Port-Based V LAN
traffic isolation: frames to/from ports 1-8 can only reach ports 1-8
  can also define V LAN based on M A C addresses of endpoints, rather than switch port
  dynamic membership: ports can be dynamically assigned among V LANs
forwarding between V LANS: done via routing (just as with separate switches)
  in practice vendors sell combined switches plus routers

## Slide 75: V LANS Spanning Multiple Switches
trunk port: carries frames between V LANs defined over multiple physical switches
  frames forwarded within V LAN between switches can’t be vanilla 802.1 frames (must carry V LAN I D info)
  802.1q protocol adds/removed additional header fields for frames forwarded between trunk ports

## Slide 76: 802.1Q V LAN Frame Format

## Slide 77: Learning Objectives (7 of 9)
6.1 introduction, services
6.2 error detection, correction
6.3 multiple access protocols
6.4 LANs
  addressing, A R P
  Ethernet
  switches
  V LANS
6.5 link virtualization: M P L S
6.6 data center networking
6.7 a day in the life of a web request

## Slide 78: Multiprotocol Label Switching (M P L S)
initial goal: high-speed I P forwarding using fixed length label (instead of I P address)
  fast lookup using fixed length identifier (rather than shortest prefix matching)
  borrowing ideas from Virtual Circuit (V C) approach
  but I P datagram still keeps I P address!

## Slide 79: M P L S Capable Routers
a.k.a. label-switched router
forward packets to outgoing interface based only on label value (don’t inspect I P address)
  M P L S forwarding table distinct from I P forwarding tables
flexibility: M P L S forwarding decisions can differ from those of I P
  use destination and source addresses to route flows to same destination differently (traffic engineering)
  re-route flows quickly if link fails: pre-computed backup paths (useful for VoIP)

## Slide 80: M P L S Versus I P Paths (1 of 2)
I P routing: path to destination determined by destination address alone

## Slide 81: M P L S Versus I P Paths (2 of 2)
I P routing: path to destination determined by destination address alone
M P L S routing: path to destination can be based on source and destination address
  fast reroute: precompute backup routes in case of link failure

## Slide 82: M P L S Signaling
modify O S P F, I S-I S link-state flooding protocols to carry info used by M P L S routing,
  e.g., link bandwidth, amount of “reserved” link bandwidth
entry M P L S router uses R S V P - T E signaling protocol to set up M P L S forwarding at downstream routers

## Slide 83: M P L S Forwarding Tables

## Slide 84: Learning Objectives (8 of 9)
6.1 introduction, services
6.2 error detection, correction
6.3 multiple access protocols
6.4 LANs
  addressing, A R P
  Ethernet
  switches
  V LANS
6.5 link virtualization: M P L S
6.6 data center networking
6.7 a day in the life of a web request

## Slide 85: Data Center Networks (1 of 3)
10’s to 100’s of thousands of hosts, often closely coupled, in close proximity:
  e-business (e.g. Amazon)
  content-servers (e.g., YouTube, Akamai, Apple, Microsoft)
  search engines, data mining (e.g., Google)
challenges:
  multiple applications, each serving massive numbers of clients
  managing/balancing load, avoiding processing, networking, data bottlenecks
Inside a 40-f t Microsoft container, Chicago data center

## Slide 86: Data Center Networks (2 of 3)
load balancer: application-layer routing
receives external client requests
directs workload within data center
returns results to external client (hiding data center internals from client)

## Slide 87: Data Center Networks (3 of 3)
rich interconnection among switches, racks:
  increased throughput between racks (multiple routing paths possible)
  increased reliability via redundancy

## Slide 88: Learning Objectives (9 of 9)
6.1 introduction, services
6.2 error detection, correction
6.3 multiple access protocols
6.4 LANs
  addressing, A R P
  Ethernet
  switches
  V LANS
6.5 link virtualization: M P L S
6.6 data center networking
6.7 a day in the life of a web request

## Slide 89: Synthesis: A Day in the Life of a Web Request
journey down protocol stack complete!
  application, transport, network, link
putting-it-all-together: synthesis!
  goal: identify, review, understand protocols (at all layers) involved in seemingly simple scenario: requesting www page
  scenario: student attaches laptop to campus network, requests/receives www.google.com

## Slide 90: A Day in the Life: Scenario

## Slide 91: A Day in the Life… Connecting to the Internet (1 of 3)
connecting laptop needs to get its own I P address, addr of first-hop router, addr of D N S server: use D H C P
D H C P request encapsulated in U D P, encapsulated in I P, encapsulated in 802.3 Ethernet
Ethernet frame broadcast (dest: F F F F F F F F F F F F) on LAN, received at router running D H C P server
Ethernet demuxed to I P demuxed, U D P demuxed to D H C P

## Slide 92: A Day in the Life… Connecting to the Internet (2 of 3)
D H C P server formulates D H C P A C K containing client’s I P address, I P address of first-hop router for client, name & I P address of D N S server
encapsulation at D H C P server, frame forwarded (switch learning) through L A N, demultiplexing at client
D H C P client receives D H C P A C K reply
Client now has I P address, knows name & addr of D N S server, I P address of its first-hop router

## Slide 93: A Day in the Life… Connecting to the Internet (3 of 3)
before sending H T T P request, need IP address of www.google.com: D N S
D N S query created, encapsulated in U D P, encapsulated in I P, encapsulated in E th. To send frame to router, need M A C address of router interface: A R P
A R P query broadcast, received by router, which replies with A R P reply giving MAC address of router interface
client now knows M A C address of first hop router, so can now send frame containing D N S query

## Slide 94: A Day in the Life… Using D N S
I P datagram forwarded from campus network into Comcast network, routed (tables created by R I P, O S P F, I S – I S and/or B G P routing protocols) to D N S server
demuxed to D N S server
D N S server replies to client with I P address of www.google.com
I P datagram containing D N S query forwarded via LAN switch from client to 1st hop router

## Slide 95: A Day in the Life…T C P Connection Carrying H T T P
to send H T T P request, client first opens T C P socket to web server
T C P S Y N segment (step 1 in 3-way handshake) inter-domain routed to web server
web server responds with T C P S Y N A C K (step 2 in 3-way handshake)
T C P connection established!

## Slide 96: A Day in the Life… H T T P Request/Reply
H T T P request sent into T C P socket
I P datagram containing H T T P request routed to www.google.com
web server responds with H T T P reply (containing web page)
I P datagram containing H T T P reply routed back to client
web page finally (!!!) displayed

## Slide 97: Chapter 6: Summary
principles behind data link layer services:
  error detection, correction
  sharing a broadcast channel: multiple access
  link layer addressing
instantiation and implementation of various link layer technologies
  Ethernet
  switched LANS, V LANs
  virtualized networks as a link layer: M P L S
synthesis: a day in the life of a web request

## Slide 98: Chapter 6: Let’s Take a Breath
journey down protocol stack complete (except P H Y)
solid understanding of networking principles, practice
….. could stop here …. but lots of interesting topics!
  wireless
  multimedia
  security

## Slide 99: Copyright