## Slide 1: Computer Networking: A Top Down Approach
Seventh Edition
Chapter 1
Introduction
Copyright © 2017, 2013, 2010 Pearson Education, Inc. All Rights Reserved
Slides in this presentation contain hyperlinks. JAWS users should be able to get a list of links by using INSERT+F7
Notes: If this PowerPoint presentation contains mathematical equations, you may need to check that your computer has the following installed:
1) MathType Plugin
2) Math Player (free versions available)
3) NVDA Reader (free versions available)

## Slide 2: Introduction (1 of 2)
Our Goal:
get “feel” and terminology
more depth, detail later in course
approach:
  use Internet as example

## Slide 3: Introduction (2 of 2)
Overview:
What’s the Internet?
What’s a protocol?
network edge; hosts, access net, physical media
network core: packet/circuit switching, Internet structure
performance: loss, delay, throughput
security
protocol layers, service models
history

## Slide 4: Learning Objectives (1 of 7)
  1.1 what is the Internet?
  1.2 network edge
  end systems, access networks, links
  1.3 network core
  packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history

## Slide 5: What’s the Internet: “Nuts and Bolts” View (1 of 2)
billions of connected computing devices:
  hosts = end systems
  running network apps
communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
packet switches: forward packets (chunks of data)
  routers and switches

## Slide 6: What’s the Internet: “Nuts and Bolts” View (2 of 2)

## Slide 7: “Fun” Internet-Connected Devices
IP picture frame
http://www.ceiva.com/
Internet
refrigerator
Slingbox: watch,
control cable TV remotely
sensorized,
bed
mattress
Web-enabled toaster +
weather forecaster
Tweet-a-watt:
monitor energy use
Internet phones

## Slide 8: What’s the Internet: “Nuts and Bolts” View
Internet: “network of networks”
  Interconnected I S Ps
protocols control sending, receiving of messages
  e.g., T C P, I P, H T T P, Skype, 802.11
Internet standards
  R F C: Request for comments
  I E T F: Internet Engineering Task Force

## Slide 9: What’s the Internet: A Service View
infrastructure that provides services to applications:
  Web, VoI P, email, games, e-commerce, social nets, …
provides programming interface to apps
  hooks that allow sending and receiving app programs to “connect” to Internet
  provides service options, analogous to postal service

## Slide 10: What’s a Protocol? (1 of 2)
human protocols:
“what’s the time?”
“I have a question”
introductions
… specific messages sent
… specific actions taken when messages received, or other events
network protocols:
machines rather than humans
all communication activity in Internet governed by protocols
protocols define format, order of messages sent and received among network entities, and actions taken on message transmission, receipt

## Slide 11: What’s a Protocol? (2 of 2)
A human protocol and a computer network protocol:
Q: other human protocols?

## Slide 12: Learning Objectives (2 of 7)
  1.1 what is the Internet?
  1.2 network edge
  end systems, access networks, links
  1.3 network core
  packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history

## Slide 13: A Closer Look at Network Structure:
network edge:
  hosts: clients and servers
  servers often in data centers
access networks, physical media: wired, wireless communication links
network core:
  interconnected routers
  network of networks

## Slide 14: Access Networks and Physical Media
Q: How to connect end systems to edge router?
residential access nets
institutional access networks (school, company)
mobile access networks
keep in mind:
bandwidth (bits per second) of access network?
shared or dedicated?

## Slide 15: Access Network: Digital Subscriber Line (D S L) (1 of 2)

## Slide 16: Access Network: Digital Subscriber Line (D S L) (2 of 2)
  use existing telephone line to central office D S L A M
      data over D S L phone line goes to Internet
      voice over D S L phone line goes to telephone net
  < 2.5 M b p s upstream transmission rate (typically < 1 M b p s)
  < 24 M b p s downstream transmission rate (typically < 10 M b p s)

## Slide 17: Access Network: Cable Network (1 of 3)
frequency division multiplexing: different channels transmitted in different frequency bands

## Slide 18: Access Network: Cable Network (2 of 3)

## Slide 19: Access Network: Cable Network (3 of 3)
H F C: hybrid fiber coax
  asymmetric: up to 30M b p s downstream transmission rate, 2 M b p s upstream transmission rate
network of cable, fiber attaches homes to I S P router
  homes share access network to cable headend
  unlike D S L, which has dedicated access to central office

## Slide 20: Access Network: Home Network

## Slide 21: Enterprise Access Networks (Ethernet)
typically used in companies, universities, etc.
10 M b p s, 100M b p s, 1G b p s, 10G b p s transmission rates
today, end systems typically connect into Ethernet switch

## Slide 22: Wireless Access Networks (1 of 2)
shared wireless access network connects end system to router
  via base station aka “access point”
wireless L A Ns:
within building (100 ft.)
802.11b/g/n (WiFi): 11, 54, 450 M b p s transmission rate

## Slide 23: Wireless Access Networks (2 of 2)
wide-area wireless access
provided by telco (cellular) operator, 10’s kilometre
between 1 and 10 M b p s
3G, 4G: L T E

## Slide 24: Host: Sends Packets of Data
host sending function:
takes application message
breaks into smaller chunks, known as packets, of length L bits
transmits packet into access network at transmission rate R
  link transmission rate, aka link capacity, aka link bandwidth

## Slide 25: Physical Media
bit: propagates between transmitter/receiver pairs
physical link: what lies between transmitter & receiver
guided media:
  signals propagate in solid media: copper, fiber, coax
unguided media:
  signals propagate freely, e.g., radio
twisted pair (T P)
two insulated copper wires
  Category 5: 100 M b p s, 1 G b p s Ethernet
  Category 6: 10G b p s

## Slide 26: Physical Media: Coax, Fiber (1 of 2)
Coaxial Cable:
two concentric copper conductors
bidirectional
broadband:
  multiple channels on cable
  H F C

## Slide 27: Physical Media: Coax, Fiber (2 of 2)
Fiber Optic Cable:
glass fiber carrying light pulses, each pulse a bit
high-speed operation:
  high-speed point-to-point transmission (e.g., 10’s-100’s G b p s transmission rate)
low error rate:
  repeaters spaced far apart
  immune to electromagnetic noise

## Slide 28: Physical Media: Radio (1 of 2)
signal carried in electromagnetic spectrum
no physical “wire”
bidirectional
propagation environment effects:
  reflection
  obstruction by objects
  interference

## Slide 29: Physical Media: Radio (2 of 2)
Radio Link Types:
terrestrial microwave
  e.g. up to 45 M b p s channels
L A N (e.g., WiFi)
  54 M b p s
wide-area (e.g., cellular)
  4G cellular: ~ 10 M b p s
Satellite
  K b p s to 45M b p s channel (or multiple smaller channels)
  270 millisec end-end delay
  geosynchronous versus low altitude

## Slide 30: Learning Objectives (3 of 7)
  1.1 what is the Internet?
  1.2 network edge
  end systems, access networks, links
  1.3 network core
  packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history

## Slide 31: The Network Core
mesh of interconnected routers
packet-switching: hosts break application-layer messages into packets
  forward packets from one router to the next, across links on path from source to destination
  each packet transmitted at full link capacity

## Slide 32: Packet-Switching: Store-and-Forward (1 of 3)

## Slide 33: Packet-Switching: Store-and-Forward (2 of 3)
takes
seconds to transmit (push out) L-bit packet into
link at R bps
store and forward: entire packet must arrive at router before it can be transmitted on next link

## Slide 34: Packet-Switching: Store-and-Forward (3 of 3)
one-hop numerical example:
L = 7.5 Mbits
R = 1.5 M b p s
one-hop transmission delay = 5 sec

## Slide 35: Packet Switching: Queueing Delay, Loss
queuing and loss:
if arrival rate (in bits) to link exceeds transmission rate of link for a period of time:
  packets will queue, wait to be transmitted on link
  packets can be dropped (lost) if memory (buffer) fills up

## Slide 36: Two Key Network-Core Functions

## Slide 37: Alternative Core: Circuit Switching (1 of 2)
end-end resources allocated to, reserved for “call” between source & dest:
in diagram, each link has four circuits.
  call gets 2nd circuit in top link and 1st circuit in right link.
dedicated resources: no sharing
  circuit-like (guaranteed) performance
circuit segment idle if not used by call (no sharing)
commonly used in traditional telephone networks

## Slide 38: Alternative Core: Circuit Switching (2 of 2)

## Slide 39: Circuit Switching: F D M Versus T D M
Notes: Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 40: Packet Switching Versus Circuit Switching (1 of 4)
packet switching allows more users to use network!
example:
1 M b/s link
each user:
  100 k b/s when “active”
  active 10% of time
circuit-switching:
  10 users

## Slide 41: Packet Switching Versus Circuit Switching (2 of 4)
packet switching:
  with 35 users, probability > 10 active at same time is less than .0004 *
Q: how did we get value 0.0004?
Q: what happens if > 35 users ?
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 42: Packet Switching Versus Circuit Switching (3 of 4)
is packet switching a “slam dunk winner?”
    great for bursty data
    resource sharing
    simpler, no call setup
  excessive congestion possible: packet delay and loss
    protocols needed for reliable data transfer, congestion control

## Slide 43: Packet Switching Versus Circuit Switching (4 of 4)
  Q: How to provide circuit-like behavior?
  bandwidth guarantees needed for audio/video apps
  still an unsolved problem (chapter 7)
Q: human analogies of reserved resources (circuit switching) versus on-demand allocation (packet-switching)?

## Slide 44: Internet Structure: Network of Networks (1 of 10)
End systems connect to Internet via access I S P s (Internet Service Providers)
  residential, company and university I S P s
Access I S Ps in turn must be interconnected.
  so that any two hosts can send packets to each other
Resulting network of networks is very complex
  evolution was driven by economics and national policies
Let’s take a stepwise approach to describe current Internet structure

## Slide 45: Internet Structure: Network of Networks (2 of 10)
Question: given millions of access I S P s, how to connect them together?

## Slide 46: Internet Structure: Network of Networks (3 of 10)
Option: connect each access I S P to every other access I S P?

## Slide 47: Internet Structure: Network of Networks (4 of 10)
Option: connect each access I S P to one global transit I S P?
Customer and provider I S P s have economic agreement.

## Slide 48: Internet Structure: Network of Networks (5 of 10)
But if one global I S P is viable business, there will be competitors ….

## Slide 49: Internet Structure: Network of Networks (6 of 10)
But if one global I S P is viable business, there will be competitors …. which must be interconnected

## Slide 50: Internet Structure: Network of Networks (7 of 10)
… and regional networks may arise to connect access nets to I S Ps

## Slide 51: Internet Structure: Network of Networks (8 of 10)
… and content provider networks (e.g., Google, Microsoft, Akamai) may run their own network, to bring services, content close to end users

## Slide 52: Internet Structure: Network of Networks (9 of 10)

## Slide 53: Internet Structure: Network of Networks (10 of 10)
at center: small of well-connected large networks
  “tier-1” commercial I S Ps (e.g., Level 3, Sprint, A T&T, N T T), national & international coverage
  content provider network (e.g., Google): private network that connects it data centers to Internet, often bypassing tier-1, regional I S Ps

## Slide 54: Tier-I I S P: e.g., Sprint

## Slide 55: Learning Objectives (4 of 7)
  1.1 what is the Internet?
  1.2 network edge
  end systems, access networks, links
  1.3 network core
  packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history

## Slide 56: How Do Loss and Delay Occur?
packets queue in router buffers
packet arrival rate to link (temporarily) exceeds output link capacity
packets queue, wait for turn

## Slide 57: Four Sources of Packet Delay (1 of 4)

## Slide 58: Four Sources of Packet Delay (2 of 4)
dproc: nodal processing
check bit errors
determine output link
typically < millisec
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router

## Slide 59: Four Sources of Packet Delay (3 of 4)

## Slide 60: Four Sources of Packet Delay (4 of 4)
dtrans: transmission delay:
L: packet length (bits)
R: link bandwidth (b p s)
dtrans
dprop: propagation delay:
d: length of physical link
s: propagation speed
dprop
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
* Check out the Java applet for an interactive animation on trans versus prop delay

## Slide 61: Caravan Analogy (1 of 3)
cars “propagate” at
toll booth takes 12 sec to service car (bit transmission time)
car ~ bit; caravan ~ packet
Q: How long until caravan is lined up before 2nd toll booth?

## Slide 62: Caravan Analogy (2 of 3)
time to “push” entire caravan through toll booth onto highway = 12×10 = 120 sec
time for last car to propagate from 1st to 2nd toll both:
A: 62 minutes

## Slide 63: Caravan Analogy (3 of 3)
suppose cars now “propagate” at
and suppose toll booth now takes one min to service a car
Q: Will cars arrive to 2nd booth before all cars serviced at first booth?
  A: Yes! after 7 min, first car arrives at second booth; three cars still at first booth

## Slide 64: Queueing Delay (Revisited) (1 of 2)
R: link bandwidth (b p s)
L: packet length (bits)
a: average packet arrival rate

## Slide 65: Queueing Delay (Revisited) (2 of 2)
than can be serviced, average delay infinite!

## Slide 66: “Real” Internet Delays and Routes
what do “real” Internet delay & loss look like?
traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
  sends three packets that will reach router i on path towards destination
  router i will return packets to sender
  sender times interval between transmission and reply.

## Slide 67: “Real” Internet Delays, Routes
Traceroute: gaia.cs.umass.edu to www.eurecom.fr
* Do some traceroutes from exotic countries at www.traceroute.org

## Slide 68: Packet Loss
queue (aka buffer) preceding link in buffer has finite capacity
packet arriving to full queue dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not at all

## Slide 69: Throughput (1 of 2)
throughput: rate (bits/time unit) at which bits transferred between sender/receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time

## Slide 70: Throughput (2 of 2)
Rs < Rc What is average end-end throughput?
Rs > Rc What is average end-end throughput?
bottleneck link
link on end-end path that constrains end-end throughput

## Slide 71: Throughput: Internet Scenario
per-connection end-end throughput:
in practice: Rc or Rs is often bottleneck
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 72: Learning Objectives (5 of 7)
  1.1 what is the Internet?
  1.2 network edge
  end systems, access networks, links
  1.3 network core
  packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history

## Slide 73: Protocol “Layers”
Networks are complex,
with many “pieces”:
Hosts
Routers
Links of various media
Applications
Protocols
Hardware, software
Question:
is there any hope of organizing structure of network?
…. or at least our discussion of networks?

## Slide 74: Organization of Air Travel
A Series of Steps

## Slide 75: Layering of Airline Functionality
layers: each layer implements a service
via its own internal-layer actions
relying on services provided by layer below

## Slide 76: Why Layering?
dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system
layering considered harmful?

## Slide 77: Internet Protocol Stack
application: supporting network applications
  F T P, S M T P, H T T P
transport: process-process data transfer
  T C P, U D P
network: routing of datagrams from source to destination
  I P, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.111 (WiFi), P P P
physical: bits “on the wire”

## Slide 78: I S O/O S I Reference Model
presentation: allow applications to interpret meaning of data, e.g., encryption, compression, machine-specific conventions
session: synchronization, checkpointing, recovery of data exchange
Internet stack “missing” these layers!
  these services, if needed, must be implemented in application
  needed?

## Slide 79: Encapsulation

## Slide 80: Learning Objectives (6 of 7)
  1.1 what is the Internet?
  1.2 network edge
  end systems, access networks, links
  1.3 network core
  packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history

## Slide 81: Network Security
field of network security:
  how bad guys can attack computer networks
  how we can defend networks against attacks
  how to design architectures that are immune to attacks
Internet not originally designed with (much) security in mind
  original vision: “a group of mutually trusting users
attached to a transparent network”
  Internet protocol designers playing “catch-up”
  security considerations in all layers!

## Slide 82: Bad Guys: Put Malware into Hosts via Internet
malware can get in host from:
  virus: self-replicating infection by receiving/executing object (e.g., e-mail attachment)
  worm: self-replicating infection by passively receiving object that gets itself executed
spyware malware can record keystrokes, web sites visited, upload info to collection site
infected host can be enrolled in botnet, used for spam. D D o S attacks

## Slide 83: Bad Guys: Attack Server, Network Infrastructure
Denial of Service (D o S): attackers make resources (server, bandwidth) unavailable to legitimate traffic by overwhelming resource with bogus traffic
select target
break into hosts around the network (see botnet)
send packets to target from compromised hosts

## Slide 84: Bad Guys Can Sniff Packets
packet “sniffing”:
broadcast media (shared Ethernet, wireless)
promiscuous network interface reads/records all packets (e.g., including passwords!) passing by
  wireshark software used for end-of-chapter labs is a (free) packet-sniffer

## Slide 85: Bad Guys Can Use Fake Addresses
I P spoofing: send packet with false source address
… lots more on security (throughout, Chapter 8)

## Slide 86: Learning Objectives (7 of 7)
  1.1 what is the Internet?
  1.2 network edge
  end systems, access networks, links
  1.3 network core
  packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history

## Slide 87: Internet History (1 of 9)
1961-1972: Early packet-switching principles
1961: Kleinrock - queueing theory shows effectiveness of packet-switching
1964: Baran - packet-switching in military nets
1967: A R P Anet conceived by Advanced Research Projects Agency
1969: first A R P Anet node operational

## Slide 88: Internet History (2 of 9)
1972:
  A R P Anet public demo
  N C P (Network Control Protocol) first host-host protocol
  first e-mail program
  A R P Anet has 15 nodes

## Slide 89: Internet History (3 of 9)
1972-1980: Internetworking, new and proprietary nets
1970: A L O H Anet satellite network in Hawaii
1974: Cerf and Kahn - architecture for interconnecting networks
1976: Ethernet at Xerox P A R C
Late70’s: proprietary architectures: D E Cnet, S N A, X N A
late 70’s: switching fixed length packets (A T M precursor)
1979: A R P Anet has 200 nodes

## Slide 90: Internet History (4 of 9)
Cerf and Kahn’s internetworking principles:
  minimalism, autonomy - no internal changes required to interconnect networks
  best effort service model
  stateless routers
  decentralized control
define today’s Internet architecture

## Slide 91: Internet History (5 of 9)
1980-1990: new protocols, a proliferation of networks
1983: deployment of T C P/I P
1982: smtp e-mail protocol defined
1983: D N S defined for name-to-I P-address translation
1985: ftp protocol defined
1988: T C P congestion control
new national networks: C Snet, B I Tnet, N S Fnet, Minitel
100,000 hosts connected to confederation of networks

## Slide 92: Internet History (6 of 9)
1990, 2000’s: commercialization, the Web, new apps
early 1990’s: A R P Anet decommissioned
1991: N S F lifts restrictions on commercial use of N S Fnet (decommissioned, 1995)
early 1990s: Web
  hypertext [Bush 1945, Nelson 1960’s]
  H T M L, H T T P: Berners-Lee
  1994: Mosaic, later Netscape
  late 1990’s: commercialization of the Web

## Slide 93: Internet History (7 of 9)
late 1990’s – 2000’s:
more killer apps: instant messaging, P2P file sharing
network security to forefront
est. 50 million host, 100 million+ users
backbone links running at G b p s

## Slide 94: Internet History (8 of 9)
2005-present
~5B devices attached to Internet (2016)
  smartphones and tablets
aggressive deployment of broadband access
increasing ubiquity of high-speed wireless access

## Slide 95: Internet History (9 of 9)
emergence of online social networks:
  Facebook: ~ one billion users
service providers (Google, Microsoft) create their own networks
  bypass Internet, providing “instantaneous” access to search, video content, email, etc.
e-commerce, universities, enterprises running their services in “cloud” (e.g., Amazon E C2)

## Slide 96: Introduction: Summary (1 of 2)
covered a “ton” of material!
Internet overview
What’s a protocol?
network edge, core, access network
  packet-switching versus circuit-switching
  Internet structure

## Slide 97: Introduction: Summary (2 of 2)
performance: loss, delay, throughput
layering, service models
security
history
you now have:
context, overview, “feel” of networking
more depth, detail to follow!

## Slide 98: Chapter 1

## Slide 99: Additional Slides

## Slide 100: Copyright